## Slide 1: State Space Models and Filtering
Daniel C

## Slide 2: Inverted Pendulum

## Slide 3: State space models
Sensor measures current state, contains noises
Model predicts future state from current state , contains disturbances
Discuss: How should we estimate the current state in real time?
Sensor
Model

## Slide 4: State space models
Filtering:
  Estimating the current state based on all information available
  Balance different sources of uncertainties
    Trust measurements more if noises are smaller than model disturbances
    Trust model predictions more if disturbances are smaller than noises

## Slide 5: Example: Random walk
E.g. Stock prices

## Slide 6: Example: Random walk
Malicious data provider

## Slide 7: Example: Random walk
How can we deduce the first graph from the second graph as much as possible?
  Previous estimation + Current observation
  Which information do we trust more?
  The general update equation:

## Slide 8: Alpha beta filter
State contains a quantity and its rate of change
E.g. Track an aircraft’s position x and velocity v
One sensor for measuring position (gaussian noise)
Velocity follows a random walk due to air resistance

## Slide 9: Alpha beta filter
Alpha: Relative trust in measurement vs prediction of position
Beta: Relative trust in measurement vs prediction of velocity
If measured position is greater than prediction, then:
  Previous estimated position is too low
  Previous estimated velocity is too low
  Some combination of both
  Measurement greater than actual position (e.g. train)

## Slide 10: Control
State at time
Control input
Dynamics:
Measurement:
  - Often have a lower dimension than the state
  - E.g. State of airplane (distribution of air pressure) vs
  measurement at a few positions

## Slide 11: Control
Variations:
  Continuous time:
Linear:
- Extensively studied
- For certain systems we can drive the system to any state
- Optimal control based on certain objectives
- Linear control law
- Koopman operator: Linearization through augmentation

## Slide 12: Control with uncertainty
Disturbances
Measurement noise
State transition:
Measurement:

## Slide 13: Filters for control
Maintain estimate of current state:
Receive measurements:
Update estimate:
We can treat K as a control system with as its state and as its input

## Slide 14: Closing the loop
The control law: )
Objectives:
    - Reach a setpoint
    - Integral cost:
  -E.g. Fuel consumption
  - Variational problem (optimize among the space of functions)

## Slide 15: Inverted Pendulum
States:
  Position
  Velocity
  Angle
  Angular velocity

## Slide 16: Inverted Pendulum
Disturbances:
  Position
  Velocity
Measurement:
  noises on all variables

## Slide 17: The kalman filter
Computes a matrix based on dynamics
Predict and update the estimate:
Minimizes the expectation error:

## Slide 18: The controller
Linear Quadratic Regulator: Computes a matrix based on cost and dynamics
Control law:
Minimizes the objective

## Slide 19: Full picture
Closed loop control with filtering